## Slide 1: A LaBr3 Fast Timing Array of NUSTAR detectors at JYFL
David M. Cullen.
School of Physics and Astronomy, University of Manchester, Manchester, M13 9PL, U.K.
NPL Meeting, March 2015

## Slide 2: UK Fast-Timing Array
Part of STFC funded NuSTAR Project to build and commission ‘stand alone’ fast-timing gamma-ray array for use with AIDA at focal plane of (S)FRS at GSI/FAIR (part of DESPEC collaboration).
People:
  U. Brighton (Alison Bruce, Oliver Roberts [PDRA])
  U. Surrey (Paddy Regan, Zsolt Podolyak, Christopher Townsley)
  U. West of Scotland (John Smith, Kieran Mullholland [PhD])
  STFC Daresbury Laboratory (Ian Lazarus-DAQ)
  U. Manchester (David Cullen, Andy Smith - design of frame).
Currently have purchased:
  31 LaBr3 detectors (2” x 1.5” cylinders)
  Cost £186,852
NPL Meeting, March 2015

## Slide 3
A Fast-Timing Array at focal plane of RITU / MARA spectrometers at University of Jyväskylä.
  Lifetimes of nuclear states populated in delayed spectroscopy
  e.g. Recoil-, proton-, isomer-, beta-, electron-tagged spectra)
NPL Meeting, March 2015

## Slide 4: Fast Timing Methods at Jyväskylä
Delayed Gammas
Isomeric state
PROMPT gammas
Isomeric state
Trigger-less Data Acquisition System
JUROGAM, RITU, GREAT and the TDR.
LaBr3 Array
NPL Meeting, March 2015

## Slide 5
Delayed γ rays but in prompt coincidence with each other (ps lifetimes)
Measure LaBr3 – LaBr3 coincidences with ~200ps intrinsic LaBr3 timing resolution.
Possible to extract lifetimes down to ~5ps (centroid shift) with good statistics.
Isomeric state (~100ns – several µs)
~ 100ps
~ 50ps
~ 5ps
Ground state
Technique
NPL Meeting, March 2015

## Slide 6
Key point: Ascertain how distribution of recoils across focal plane affects measurement of short ps lifetimes.
  e.g. 2 events separated by a few cm will have different gamma transit times (of order of ~ps) to reach the same detector.
  This can be somewhat corrected for by first calibrating the effect using source measurements from various positions across the DSSD.
  However, this assumes you know the recoil position in the DSSD. This is easy for alpha, beta tagging, but not so obvious for isomer tagging.
  This needs physics input from community now.
LaBr3 Project JYFL
NPL Meeting, March 2015
Status: 5 days beam time approved to test 8 LaBr3 detector array to measure lifetimes fed by delayed/isomer spectroscopy at focal plane of RITU. Experiment will likely take place in the summer 2015.
  If test is successful, then we may want to investigate the possibility to place up to 28 detectors (geometry permitting) around the focal plane for campaigns of physics experiments with RITU/MARA... in ~2016/2017/2018?

## Slide 7
NPL Meeting, March 2015
Test Experiment 138Gd
T1/2 = 6µs
308(17) ps
13(3) ps
3.8(15) ps
1.8(4) ps
Plunger T1/2
Cross section ~100mb to 138Gd and 1% to K=8 isomer ~ 1mb
106Cd(36Ar,2p2n)138Gd reaction

## Slide 8
Timing setup - 1 TAC per detector
Planar removed but
still have clover detector above
NPL Meeting, March 2015

## Slide 9
8 Detector setup
NPL Meeting, March 2015
All detectors are 100mm from DSSD to LaBr front face (compared with 70mm if pack 2 directly at back as close as possible).

## Slide 10
Count distribution in the 8 detectors
View from the back
View from the top
8 LaBr3 Design Simulation
Marc Labiche
NPL Meeting, March 2015
138Gd isomer
Range 200-600 keV

## Slide 11
8 detector LaBr3 frame design (D. Seddon)
NPL Meeting, March 2015
Bolts onto existing JYFL blue frame

## Slide 12
Possibilities after this 8 detector test experiment?
NPL Meeting, March 2015

## Slide 13
Chart: Gamma-ray Energy [MeV]
| 0.1 | 0.30000000000000032 | 0.5 | 0.8 | 1 | 1.4 | 1.8 | 2.5
Same as above with most detectors tilted | 3.0145 | 3.875 | 2.9095 | 2.0135 | 1.773 | 1.387 | 1.1925 | 0.9035
Same as above with tilted detector and without planar detector. | 9.785 | 6.765 | 4.35 | 2.9045 | 2.3765 | 1.8275 | 1.519 | 1.1995
M. Labiche
Remove planar when not needed?
NPL Meeting, March 2015
138Gd isomer
Range 200-600 keV

## Slide 14
Cross sections accessible with a larger array?
However, in the mean time can make order of magnitude estimate.
Assume:
Each LaBr detector has efficiency 0.5%
DSSD efficiency for recoil detection ~ 80%
If require 1000 counts in a peak to use centroid shift method, this means:
g-g-g analysis requires 1000/(0.8*0.0053) ~ 1010 recoils
g-g analysis requires 1000/(0.8*0.0052) ~ 50x106 recoils
Using R = N φ σ and RITU transport efficiency of 30% for typical reaction
(5pnA beam on 1mg/cm2 target for 7 days),
Gives cross section estimated limits for
LaBr-LaBr-LaBr coincidences is ~ 500 mb
LaBr-LaBr-Clover coincidences is ~50 mb (using clover efficiency=5%)
LaBr-LaBr coincidences is ~ 3 mb.
Need to start to think about physics ideas to Dave.cullen@manchester.ac.uk
NPL Meeting, March 2015
This can only really be fully known once the results of the test experiment are Validated against the test experiment simulation.

## Slide 15: Thanks to…
M. Labiche, D. Seddon, D.M.Cullen, A.Smith, M. Taylor, C.Scholey, P.Greenlees, P.Rahkila, R.Julin,
and the
UK-NUSTAR Collaboration (A.M. Bruce, Z. Podolyak, P. Regan,...)
Physics ideas to Dave.cullen@manchester.ac.uk